## Slide 1: Focus Crash and Facility Type (FCFT): Practitioner Workshop
Eric Donnell
Vikash Gayah
Pennsylvania State University
Frank Gross
Thanh Le
VHB
November 3, 2021

## Slide 2: Disclaimer
This presentation was created and is being presented by contractors. The views and opinions expressed in this presentation are the presenters’ and do not necessarily reflect those of the Federal Highway Administration (FHWA) or the U.S. Department of Transportation (USDOT). The contents do not necessarily reflect the official policy of the USDOT.
The U.S. Government does not endorse products or manufacturers. Trademarks or manufacturers’ names appear in this presentation only because they are considered essential to the objective of the presentation. They are included for informational purposes only and are not intended to reflect a preference, approval, or endorsement of any one product or entity.

## Slide 3: Purpose of the Workshop and Learning Objectives

## Slide 4: Workshop Purpose
Provide an overview of data, methods, and results of FHWA Report, Contributing Factors for Focus Crash and Facility Types (FHWA-HRT-20-052).(1)
Identify opportunities for agency practices and future research to build on FHWA FCFT methods and findings.

## Slide 5: Today’s Learning Objectives
Discover the systemic approach and its application to highway safety.
Recognize the role of data in the systemic approach.
Identify resources that can support the systemic approach.
Learn about risk factors and how they are identified and inform the systemic approach.
Share challenges and best practices with peers.

## Slide 6: Workshop Icons
Information from Contributing Factors for Focus Crash and Facility Types report and quick reference guide, or The Development of Crash Modification Factors: Highway Safety Statistical Paper Synthesis report.(1,2,3)
Applications and extensions of methods presented in the FHWA FCFT report.(1)
Source: FHWA.

## Slide 7: Questions?
?
Please ask in the chat panel.
Source: FHWA.

## Slide 8: Workshop Outline
Present an overview of the systemic approach of FCFT.
Identify FCFTs:
  Review the FHWA FCFT study.
  Develop your own FCFTs.
Identify and evaluate risk factors:
  Provide examples from FHWA FCFT study.
  Identify agency-specific risk factors.
Screen and prioritize candidate locations.
Select countermeasures.
Hold discussions.

## Slide 9: Polling Question
Q1
From what region are you calling?
Source: FHWA.
Notes: Brief intro/engagement slide – what State are you calling in from today?
Poll: What region are you calling in from:
North
Midwest
South
West
Something else

## Slide 10: Polling Question
Q2
Does your State use the systemic approach?
Source: FHWA.
Notes: Does your State use the systemic method? Answers: Yes/No/Not sure
Plan to have specific targeted follow-up – e.g., for those agencies who don’t use systemic, would you be willing to provide explanation of the challenges/barriers or other reasons why

## Slide 11: Systemic Definition
All photos source: FHWA.
Systemic method identifies and proactively treats sites with certain features that are more conducive to safety problems, including sites without any problems observed yet.
“Systemic safety improvement” means a proven safety countermeasure(s) that is widely implemented based on high-risk roadway features that are correlated with particularly severe crash types.(4)

## Slide 12: Overview of the Systemic Approach
Source: FHWA. Modified by FHWA.(5)

## Slide 13: Polling Question
Q3
Are you familiar with the terms focus crash type and facility type?
Source: FHWA.
Notes: Are you familiar with the term focus crash type? Yes/No/I’ve heard it before but not sure what it means

## Slide 14: Polling Question
Q4
How does your agency identify focus crash type and facility type?
Source: FHWA.
Notes: Open question for chatbox

## Slide 15: Systemic Approach: Select Focus Crash Types
What does “focus crash type” mean?
  It is a crash type that represents the greatest number of severe crashes across the roadway system of interest.
  It provides the greatest potential to reduce fatalities and severe injuries:
    Roadway departure (RwD).
    Intersection.
    Pedestrian.
    Speed.
Chart: 
 | 0.47436 | 0.17158 | 0.11357 | 0.11274 | 0.12775
US Fatalities by FHWA Focus Area
(FARS 2014–2016)
Source: National Highway Traffic Safety Administration (NHTSA) data. Created by FHWA.(6)
Ped = pedestrian; FARS = Fatality Analysis Reporting System.

## Slide 16: Systemic Approach: Select Focus Facilities
What does “focus facility” mean?
  A facility type where the focus crash type most frequently occurs:
    Rural, two-lane highways.
    Urban, signalized intersections.
    Horizontal curves.
    Rural, thru-stop intersections.
Source: FHWA. Modified by FHWA.(5)

## Slide 17: FHWA FCFT Study Objectives
Select reliable and applicable data resources, statistical methodologies, analysis procedures, and tools.
Conduct data analysis to identify and validate FCFTs and their associated contributing factors.
Identify potential low-cost safety strategies that may effectively be used as systemic safety improvements.
Develop a technical report and a quick reference guide for identifying focus crash types and contributing factors.
Develop a solicitation and evaluation criteria to identify volunteer agencies to implement systemic safety improvements.

## Slide 18: FHWA FCFT Report: Identifying FCFTs
Data sources:
FARS: 2010–2014:(6)
  Accident data file.
  Vehicle data file.
  Person data file.
Highway Safety Information System (HSIS):(7) 2009–2014 data from Washington, Ohio, California, and Minnesota:
  Accident data file.
  Roadway data file.
  Intersection data file (only needed for California).
  Curve data file (only needed for Washington).
Source: NHTSA.
Source: HSIS.(7)

## Slide 19: FHWA FCFT Report: Identifying FCFTs
Define potential FCFTs by the various combinations of:
Crash type.
Area type (rural or urban).
Roadway type.
Location (intersection or non-intersection).
Intersection type (four-leg or T- or Y-intersection).
Type of traffic control (stop-controlled or signalized).
Lighting (day versus night).
Road alignment (horizontal curve versus straight/tangent).
All art source: FHWA.

## Slide 20: FHWA FCFT Report: Identifying FCFTs
Rank potential FCFTs by:
  Number of fatal crashes (K).
  Fatal plus serious injury crashes (KA) for the HSIS States.
  Develop separate ranked lists to assess ranking consistency based on:
  FARS data.
  Data for each of the HSIS States.
Compare with the results of the process from FHWA’s Systemic Safety Project Selection Tool.(5)
Source: FHWA.

## Slide 21: FHWA FCFT Report: Identifying FCFTs
Example Crash Count Ranking: Potential Non-Intersection FCFTs From FARS(1)
No. | Crash Type | Area Type | Roadway Type | Light Conditions | Road Alignment | K Crashes
1 | Fixed object | Rural | 2-lane road | Nighttime | Curve | 5,197
2 | Fixed object | Rural | 2-lane road | Daylight | Curve | 4,095
3 | Fixed object | Rural | 2-lane road | Nighttime | Straight | 4,094
4 | Fixed object | Rural | 2-lane road | Daylight | Straight | 3,825
5 | Head-on | Rural | 2-lane road | Daylight | Straight | 2,789
6 | Pedestrian | Urban | Multilane divided | Nighttime | Straight | 2,174
7 | Pedestrian | Urban | Multilane undivided | Nighttime | Straight | 2,118
8 | Pedestrian | Urban | 2-lane road | Nighttime | Straight | 2,051
9 | Pedestrian | Rural | 2-lane road | Nighttime | Straight | 1,918
10 | Angle | Rural | 2-lane road | Daylight | Straight | 1,815

## Slide 22: FHWA FCFT Report: Identifying FCFTs
Example Crash Count Ranking: Potential Intersection FCFTs From FARS(1)
No. | Crash Type | Area Type | Roadway Type | Int. Type | Traffic Control | Light Conditions | K Crashes
1 | Angle | Rural | 2-lane road | 4-leg | Stop Cntrl | Daylight | 2,424
2 | Angle | Urban | 2-lane road | 4-leg | Stop Cntrl | Daylight | 1,126
3 | Angle | Urban | Multilane divided | 4-leg | Signalized | Daylight | 977
4 | Angle | Urban | Multilane undivided | 4-leg | Signalized | Daylight | 864
5 | Angle | Rural | 2-lane road | 4-leg | Stop Cntrl | Nighttime | 750
6 | Angle | Urban | Multilane divided | 4-leg | Signalized | Nighttime | 684
7 | Angle | Rural | 2-lane road | T-Int | Stop Cntrl | Daylight | 592
8 | Pedestrian | Urban | Multilane divided | 4-leg | Signalized | Nighttime | 589
9 | Angle | Urban | Multilane undivided | 4-leg | Signalized | Nighttime | 555
10 | Angle | Urban | 2-lane road | T-Int | Stop Cntrl | Daylight | 536
T-Int = T-intersection; Cntrl = control.

## Slide 23: FHWA FCFT Report: Identifying FCFTs
Example Crash Count Ranking: Potential Non-Intersection FCFTs From HSIS Ohio Data (by KA Crashes)(1)
No. | Crash Type | Area Type | Roadway Type | Light Conditions | Road Alignment | KA Crashes
1 | Fixed object | Rural | 2-lane roads | Daylight | Straight | 1,027
2 | Fixed object | Rural | 2-lane roads | Nighttime | Straight | 792
3 | Fixed object | Rural | 2-lane roads | Daylight | Curve | 773
4 | Fixed object | Urban | Freeways | Daylight | Straight | 590
5 | Fixed object | Rural | 2-lane roads | Nighttime | Curve | 569
6 | Rear end | Urban | Freeways | Daylight | Straight | 565
7 | Fixed object | Urban | Freeways | Nighttime | Straight | 522
8 | Rear end | Rural | 2-lane roads | Daylight | Straight | 409
9 | Sideswipe—meeting | Rural | 2-lane roads | Daylight | Straight | 391
10 | Sideswipe—passing | Urban | Freeways | Daylight | Straight | 348

## Slide 24: FHWA FCFT Report: Identifying FCFTs
Example Crash Count Ranking: Potential Intersection FCFTs From HSIS Ohio Data (by KA Crashes)(1)
No. | Crash Type | Area Type | Roadway Type | Location Type | Light Conditions | K Crashes | KA Crashes
1 | Angle | Rural | 2-lane roads | Intersection | Daylight | 153 | 1,152
2 | Angle | Urban | Multilane undivided | Intersection | Daylight | 29 | 657
3 | Angle | Urban | Multilane divided | Intersection | Daylight | 33 | 511
4 | Rear end | Urban | Multilane undivided | Intersection | Daylight | 10 | 338
5 | Angle | Rural | 2-lane roads | Intersection | Nighttime | 48 | 296
6 | Angle | Urban | Multilane divided | Intersection | Daylight | 27 | 243
7 | Rear end | Urban | 2-lane roads | Intersection | Daylight | 5 | 243
8 | Angle | Urban | Multilane undivided | Intersection | Nighttime | 10 | 242
9 | Angle | Rural | 2-lane roads | Intersection | Daylight | 25 | 213
10 | Rear end | Rural | 2-lane roads | Intersection | Daylight | 13 | 205

## Slide 25: FHWA FCFT Report: Identifying FCFTs
Run-off-road (ROR) crashes on rural two-lane roads on horizontal curves (daytime and nighttime).
ROR crashes on rural two-lane roads on straight segments (daytime and nighttime).
Lane-departure crashes on rural two-lane roads on horizontal curves (daytime and nighttime).
Lane-departure crashes on rural two-lane roads on straight segments (daytime and nighttime).
Head-on crashes on rural two-lane roads on horizontal curves (daytime and nighttime).
Head-on crashes on rural two-lane roads on straight segments (daytime and nighttime).
Rollover crashes on rural two-lane roads on straight segments (daytime and nighttime).
Rollover crashes on rural two-lane roads on horizontal curves (daytime and nighttime).
Angle crashes on rural two-lane roads on straight segments (daytime).
List of Non-Intersection FCFTs

## Slide 26: FHWA FCFT Report: Identifying FCFTs
  Angle crashes on rural two-lane roads at four-leg stop-controlled intersections (daytime and nighttime).
  Angle crashes on urban two-lane roads at four-leg stop-controlled intersections (daytime).
  Angle crashes on urban multilane divided roads at four-leg signalized intersections (daytime).
  Angle crashes on urban multilane undivided roads at four-leg signalized intersections (daytime).
  Angle crashes on rural two-lane roads at three-leg stop-controlled intersections (daytime).
  Angle crashes on rural multilane divided roads at four-leg minor-road stop-controlled intersections (daytime).
List of Intersection FCFTs

## Slide 27: FHWA FCFT Report: Identifying FCFTs
Crash Type | Conditions |  |  | 
Crash Type | Horizontal Curve | Straight | Daylight | Nighttime
ROR |  |  |  | 
 |  |  |  | 
Lane Departure |  |  |  | 
 |  |  |  | 
Head-on |  |  |  | 
 |  |  |  | 
Angle |  |  |  | 
Rollover/Overturn |  |  |  | 
 |  |  |  | 
Non-Intersection FCFTs on Rural, Two-Lane Roads
 = conditions that defined focus crash types.

## Slide 28: FHWA FCFT Report: Identifying FCFTs
Intersection FCFTs
Crash Type | Conditions |  |  |  |  |  |  |  |  |  | 
Crash Type | Urban | Rural | Two-Lane | Multilane Divided | Multilane Undivided | 4-Leg | 3-Leg | Stop Controlled | Signalized | Daylight | Nighttime
Angle |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  Minor road |  |  | 
 = conditions that defined focus crash types.

## Slide 29: FHWA FCFT Report: Identifying FCFTs
Results: Pedestrian FCFTs (information from related published literature):
  All types of pedestrian crashes at intersections.
  Pedestrian crashes at intersections involving a crossing pedestrian and a vehicle going straight.
Source: FHWA.

## Slide 30: Developing Agency-Specific FCFTs
Analyze data to identify crash and facilities types.
Compile data.
  Use data from crash reports. OR
  Combine crash data with roadway inventory and other data sources.
Source: FHWA.

## Slide 31: Data Sources
Roadway inventory data—Typically maintained by State and local agencies:
  Facility type.
  Number of lanes.
  Cross-sectional elements.
  Traffic control and speed limit.
Traffic data—Typically maintained by State and local agencies, although some manual counts may be needed:
  Traffic volume.
  Nonmotorized user exposure.
  Traffic composition.
Crash data—Typically maintained by State agencies:
  Number of crashes by type.
  Number of crashes by severity.
All art source: FHWA.

## Slide 32: Option 1: Using Crash Reports
Relevant data fields:
  Intersection type.
  Roadway type.
  Traffic control device.
  Crash type.
  Speed limit.
  Illumination type.
  Indicators for:
    Work zone.
    School bus/zone related.
Source: FHWA.

## Slide 33: Option 2: Merging Data
Data sources and information are needed as follows:
  Roadway inventory data:
    Facility type.
    Number of lanes.
    Cross-sectional elements.
    Traffic control and speed limit.
  Traffic data:
    Traffic volume.
    Nonmotorized user exposure.
    Traffic composition.
  Crash data:
    Number of crashes by type.
    Number of crashes by severity.
Analysis database must be developed to identify FCFTs.
Each “row” or observation should represent a single crash that was observed.
Each crash observation should be linked to the roadway and traffic characteristics based on where the crash occurred—The linear referencing system can be used.

## Slide 34: Polling Question
Q5
Are you familiar with a linear referencing system?
Source: FHWA.
Notes: Are you familiar with a linear referencing system?
-Yes, I use if often
-Yes, but it’s not something I typically work with
-No, I’ve never heard this term before
-Not sure, I’ve heard this term but not sure what it means

## Slide 35: What Is a Linear Referencing System?
Source: FHWA.

## Slide 36: Merging Crash and Roadway Data for FCFT Identification
Road Log File
Crash File
What were the roadway and traffic characteristics associated with each crash?
County | Route | Beg_MP | End_MP | Lanes | Lane Width | Shld Width
12 | 322 | 0 | 1.25 | 2 | 12 | 6
12 | 322 | 1.25 | 2.45 | 4 | 11 | 8
12 | 322 | 2.45 | 3.05 | 4 | 12 | 6
12 | 322 | 3.05 | 4.03 | 4 | 11 | 6
Crash ID | County | Route | MP | Severity
654 | 12 | 322 | 1.75 | 4
4556 | 12 | 322 | 3.35 | 5
5426 | 12 | 322 | 0.75 | 3
6241 | 12 | 322 | 2.65 | 3
7412 | 12 | 322 | 2.85 | 4
8641 | 12 | 322 | 3.75 | 5
9715 | 12 | 322 | 0.65 | 3
Beg = beginning; MP = milepost; Shld = shoulder; ID = identification.

## Slide 37: Merging Crash and Roadway Data for FCFT Identification
Road Log File
Crash File
County | Route | Beg_MP | End_MP | Lanes | Lane Width | Shld Width
12 | 322 | 0 | 1.25 | 2 | 12 | 6
12 | 322 | 1.25 | 2.45 | 4 | 11 | 8
12 | 322 | 2.45 | 3.05 | 4 | 12 | 6
12 | 322 | 3.05 | 4.03 | 4 | 11 | 6
Crash ID | County | Route | MP | Severity
654 | 12 | 322 | 1.75 | 4
4556 | 12 | 322 | 3.35 | 5
5426 | 12 | 322 | 0.75 | 3
6241 | 12 | 322 | 2.65 | 3
7412 | 12 | 322 | 2.85 | 4
8641 | 12 | 322 | 3.75 | 5
9715 | 12 | 322 | 0.65 | 3
Crash ID | County | Route | MP | Severity | Lanes | Lane Width | Shld Width
654 | 12 | 322 | 1.75 | 4 | 4 | 11 | 8
4556 | 12 | 322 | 3.35 | 5 | 4 | 11 | 6
5426 | 12 | 322 | 0.75 | 3 | 2 | 12 | 6
6241 | 12 | 322 | 2.65 | 3 | 4 | 12 | 6
7412 | 12 | 322 | 2.85 | 4 | 4 | 12 | 6
8641 | 12 | 322 | 3.75 | 5 | 4 | 11 | 6
9715 | 12 | 322 | 0.65 | 3 | 2 | 12 | 6
Notes: VG question: Do we want to make up another data example where roadway features changed? That might be more helpful to demonstrate the “merge” required in this case?

## Slide 38: Exercise: Identify FCFTs
Notes: Conduct a live exercise using real data. Create crash tree from data and ask participants to identify FCFTs

## Slide 39: Exercise: Identify FCFTs From Crash Tree
Generate crash tree from data.
Identify FCFTs.
Source: FHWA.
Crash tree generated using R(8) and vtree package.(9)
Notes: Conduct a live exercise using real data. Create crash tree from data and ask participants to identify FCFTs

## Slide 40: Polling Question
Q6
What are FCFTs in your State (e.g., from similar analyses, from Strategic Highway Safety Plan (SHSP), from other strategic program efforts)?
Source: FHWA.
Notes: Open questions for chatbox

## Slide 41: Systemic Approach: Identify and Evaluate Risk Factors
What does “risk factor” mean?
  A representation of risk in terms of the characteristics associated with locations where targeted crash types occurred:
    Traffic volume.
    Roadway geometry (number of lanes, lane width, curvature).
    Traffic operations (speed, traffic control, signs, markings).
    Roadside design (clear zone, sight distance).
All photos source: FHWA.

## Slide 42: Systemic Approach: Identify and Evaluate Risk Factors
Source: FHWA.

## Slide 43: Systemic Approach: Identify and Evaluate Risk Factors
Source: FHWA.

## Slide 44: FHWA FCFT Report: Risk Factors
Three States:
  California and Ohio data for non-intersection
  crashes.
  Washington and Ohio data for intersection
  crashes.
Data sources:
  Roadway and traffic data from HSIS.
  Climate data from National Oceanic and Atmospheric Administration.
  Socioeconomic data from U.S. Census Bureau.
Source: FHWA.

## Slide 45: FHWA FCFT Report: Risk Factors
Integrate data from different sources:
  Designate plot study locations for each State:
    Intersections.
    Curve segments.
    Tangent segments.
  Join climate data:
    Use nearest weather station.
    Base on straight line distance.
  Join census data:
    Use census block containing study site.
    Use the midpoint for roadway segment.
All art source: FHWA.

## Slide 46: FHWA FCFT Report: Risk Factors
Potential contributing factors defined by three categories:
  Roadway.
  Climate.
  Census.
  Philosophy of causation or causal inference not implied:
  Some could be direct contributing factors.
  Others may be surrogates for other characteristics.
  Consistency considered:
  Across subsets of related FCFTs.
  Across multiple States.
  With previous findings in the literature.

## Slide 47: FHWA FCFT Report: Roadway Risk Factors
  Annual average daily traffic (AADT) (average, mainline/major, cross street/minor).
  Segment length.
  Curve radius.
  Percent grade.
  Grade type.
  Shoulder type.
  Terrain.
  Speed limit.
  Width (lane, shoulder, median, and surface).
  Truck percentages.
  Mainline left-/right-turn channelization.
  Cross-street left-/right-turn channelization.
  Number of approaches with left-/right-turn lanes.

## Slide 48: FHWA FCFT Report: Climate Risk Factors
Potential climate contributing factors:
  Average annual number of days with temperature ≤32℉.
  Average annual snowfall totals.
  Average annual rainfall totals.
  Average annual maximum and minimum temperatures.
  Average annual winter minimum temperatures.
All art source: FHWA.

## Slide 49: FHWA FCFT Report: Socioeconomic Risk Factors
Source: FHWA.

## Slide 50: FHWA FCFT Report: Identify Risk Factors
Methodology of random forest:
  Tree-based machine-learning
  algorithm:
    Binary tree mapping a response variable and explanatory variables.
    Output in the form of a tree showing the predictive splits.
  Multiple trees to form a random forest:
    Aggregated results.
    Random forest plots: displaying the increase in MSE with removal of a variable.
    Most influential variables indicated.
Source: FHWA.

## Slide 51: FHWA FCFT Report: Identify Risk Factors
Use the random forest algorithm to identify the strongest predictors (highest percent increase in MSE).
  Example: ROR crashes on rural two-lane horizontal curves.
Source: FHWA.(1)
%IncMSE = percent increase in MSE.

## Slide 52: FHWA FCFT Report: Identify Risk Factors
Determine the direction of the relationship between the outcome variable (e.g., crash frequency) and each predictor:
  Plots of random forest predicted crash.
  Example: Angle crashes versus mainline AADT.
Source: FHWA.(1)

## Slide 53: FHWA FCFT Report: Identify Risk Factors
Contributing Factors for Daytime, ROR Crashes That Resulted in Fatal, Incapacitating, or Non‐Incapacitating Injury (ROR-KAB-D) on Rural, Two-Lane Tangent Sections: Washington State(1)
Variable | Impact on Crash Frequency Predictions
Percent Grade | Increases
Average AADT | Increases
Truck Percentage | Decreases
Average Shoulder Width | Decreases
Average Annual Rainfall Total | Increases
Percentage of Population (Ages 20–44 yr) | Increases
Percentage of People (Ages 16–24 yr) Unemployed | Increases
Annual Average Maximum Temperature | Decreases
Percentage of Population (Ages 25+ yr) with High School Diploma (But No University Degree) | Decreases
Percentage of Population (Ages 25+ yr) without High School Diploma | Decreases

## Slide 54: FHWA FCFT Report: Identify Risk Factors
Contributing Factors for Nighttime, Head-on Crashes That Resulted in Fatal, Incapacitating, or Non‐Incapacitating Injury (HEO-KAB-N) on Rural, Two-Lane Horizontal Curves: Washington State(1)
Variable | Impact on Crash Frequency Predictions
Percentage of Population (Ages 15–19 yr) | Increases
Truck Percentage | Decreases
Average AADT | Increases
Percentage of Population (Ages 25+ yr) with High School Diploma (But No University Degree) | Decreases
Average Shoulder Width | Increases
Percentage of People (Ages 16–24 yr) Working Part Time | Decreases
Percentage of Households with One Vehicle | Decreases
Percentage of Households with Income > $100,000 | Increases
Annual Average Maximum Temperature | Decreases
Percentage of Population (Ages 65–74 yr) | Decreases

## Slide 55: FHWA FCFT Report: Identify Risk Factors
Contributing Factors for Daytime, Angle Crashes That Resulted in Fatal, Incapacitating, or Non‐Incapacitating Injury (ANG-KAB-D) on Rural, Two-Lane Horizontal Curves and Tangent Sections: Ohio(1)
Variable | Impact on Crash Frequency Predictions
Percent Grade | Decreases
Average AADT | Increases
Percentage of Population (Ages 25+ yr) with University Degree | Increases
Percentage of Households with Income > $100,000 | Increases
Percentage of Population (Ages 25+ yr) without High School Diploma | Increases
Percentage of Population (Ages 45–64 yr) | Decreases
Surface Width | Increases
Percentage of Population (Ages 25+ yr) with High School Diploma (But No University Degree) | Decreases
Percentage of Population (Ages 20–44 yr) | Increases
Percentage of Population (Ages 75+ yr) | Decreases

## Slide 56: FHWA FCFT Report: Identify Risk Factors
Contributing Factors for Daytime, Angle Crashes That Resulted in Fatal, Incapacitating, or Non-Incapacitating Injury (ANG-KAB-D) at Four-Leg Signalized Intersections on Urban, Multilane Divided Roads: California(1)
Variable | Impact on Crash Frequency Predictions
Average Annual Rainfall Total | Decreases
Percentage of Households with Income < $50,000 | Increases
Annual Average Winter Minimum Temperature | Decreases
Annual Average Minimum Temperature | Decreases
Annual Average Number of Days with Minimum Temperature ≤ 32℉ | Decreases
Design Speed | Increases
Lane Width | Increases
Percentage of Population (Ages 75+ yr) | Increases
Mainline AADT | Increases
Median Width | Increases

## Slide 57: FHWA FCFT Report: Identify Risk Factors
Contributing Factors for Daytime, Angle Crashes That Resulted in Fatal, Incapacitating, or Non-Incapacitating Injury (ANG-KAB-D) at Four-Leg Stop Controlled Intersections on Rural, Multilane Divided Roads: Ohio(1)
Variable | Impact on Crash Frequency Predictions
Speed Limit | Decreases
Mainline AADT | Increases
Cross Street AADT | Decreases
Average Annual Snowfall Total | Increases
Annual Average Maximum Temperature | Decreases
Percentage of Households with Income between $50,000 and $100,000 | Decreases
Average Annual Rainfall Total | Increases
Percentage of Households with Income > $100,000 | Increases
Percentage of People (Ages 16–24 yr) Unemployed | Increases
Percentage of Population (Ages 25+ yr) with University Degree | Decreases

## Slide 58: Questions
Q7
Do you see anything missing from this list of risk factors?
What are advantages and challenges of weather and socioeconomic factors?
Risk Factors for ROR-KAB-D on Rural, Two-Lane Tangent Road in Washington State
Average AADT
Truck Percentage
Average Shoulder Width
Average Annual Rainfall Total
Percentage of Population (Ages 20–44 yr)
Percentage of People (Ages 16–24 yr) Unemployed
Annual Average Maximum Temperature
Percentage of Population (Ages 25+ yr) with High School Diploma (But No University Degree)
Percentage of Population (Ages 25+ yr) without High School Diploma
Source: FHWA.
Notes: Open questions for chatbox

## Slide 59: What Have We Covered?
Overview of the systemic approach.
Focus crash facility types:
  Overview of FHWA FCFT study.
  Development of agency-specific FCFTs.
Risk factors:
  Identify and evaluate risk factors.
  Summarize FHWA FCFT study findings.
  After a 15-min break, a live demonstration/exercise: Risk factor identification using random forest.
Notes: Conduct a live exercise using real data

## Slide 60: Break
15 min
Source: FHWA.

## Slide 61: Exercise: Identify Risk Factors
Notes: Conduct a live exercise using real data. Run Random Forest model and ask participants to identify FCFTs

## Slide 62: Exercise: Identify Risk Factors
Run random forest model.
Generate variable importance chart.
Identify risk factors.
Source: FHWA.
Model generated using R(8) and randomForest package.(10)
Notes: Conduct a live exercise using real data. Run Random Forest model and ask participants to identify FCFTs

## Slide 63: Quantifying Agency-Specific Risk Factors
Compile data.
Analyze data to quantify risk factors.
Source: FHWA.

## Slide 64: Data Sources
Roadway inventory data—Typically maintained by State and local agencies:
  Facility type.
  Number of lanes.
  Cross-sectional elements.
  Traffic control and speed limit.
Traffic data—Typically maintained by State and local agencies, although some manual counts may be needed:
  Traffic volume.
  Nonmotorized user exposure.
  Traffic composition.
Crash data—Typically maintained by State agencies:
  Number of crashes by type.
  Number of crashes by severity.
All art source: FHWA.

## Slide 65: Linking Data
Analysis database represents individual roadway segments/intersections of interest that were identified as an FCFT.
Each “row” or observation should represent a roadway element.
Crashes should be assigned to each roadway element—A linear referencing system can be used.
All art source: FHWA.

## Slide 66: Merging Roadway and Crash Data
Use the linear referencing system:
  Find county, route, and MP.
  Start with the road log file as the “base” and append the crash data (must account for segments or intersections with “zero” crash frequency).
Road Log File
Accident File
Source: HSIS.(7)
How many crashes per segment?

## Slide 67: Data Merge Solution
County-Route | Begin MP | End MP | Number of Crashes
0030000049 | 0 | 0.251 | 0*
0030000049 | 0.251 | 1.42 | 1
0030000049 | 1.42 | 2.03 | 4
0030000049 | 2.03 | 2.13 | 0*
0030000049 | 2.13 | 2.69 | 2
0030000049 | 2.69 | 3.13 | 0*
0030000049 | 3.13 | 3.69 | 1
0030000049 | 3.69 | 4.21 | 0*
0030000049 | 4.21 | 4.503 | 0*
*Must retain 0’s
Source: HSIS.(7)

## Slide 68: Data Analysis
Risk factors can be quantified using statistical methods. Examples in this workshop include:
  Logistic regression.
  Negative binomial (NB) regression and NB variants.
  Combination of data partitioning and statistical models.
FHWA Highway Safety Statistical Paper Synthesis report includes:(3)
Alternative data sources and methods for application in safety management process.
  Methods for predication/estimation (e.g., safety performance function or risk factor identification) and for evaluation (e.g., crash modification factors (CMFs) or program evaluation).
Source: FHWA.(3)

## Slide 69: Logistic Regression
Definition: Binary outcome that provides probability of one or more crashes occurring at a location during a given time as function of a set of explanatory variables.
Strength: Quantifies crash risk at a location that is associated with particular features of that location.
Limitation: Does not account for count nature of crash frequency data.
Relevance to systemic safety: Identifies how changes in risk factors influence the probability of one or more crashes at a location.

## Slide 70: NB Regression
Definition: Count model that assumes an exponential relationship between predicted crash frequency and a set of explanatory variables. Accounts for the overdispersion often seen in crash data.
Strength: Produces an equation that practitioners can used to predict crash frequency as a function of a location’s features.
Strength of approach: Can determine how each risk factor influences predicted crash frequency.
Limitation of approach: Other count regression methods may offer improvements over NB models.
Relevance to systemic approach: Quantifies the relationship between risk factors and the predicted number of crashes.

## Slide 71: Extensions to the Traditional NB Model Have Been Used to Account for Issues in Crash Data
Example issues:
  NB functional form does not adequately fit crash data.
  Data are temporally and/or spatially correlated.
  Safety-influencing explanatory variables are not available (i.e., unobserved heterogeneity).
All art source: FHWA.

## Slide 72: Extensions to NB Modeling
Examples include the following:
  Alternative functional form of model.
  Random parameters to capture unobserved heterogeneity.
  Model-based recursive partitioning algorithm.
Strengths include the following:
  Better “fit” to reported crash data.
  Improved interpretation of risk factors.
Limitations include the following:
  More difficult to estimate.
  Transferability to data not used to estimate models is uncertain.
Extensions should be applied when making safety decisions using agency-specific data.
Information available in FHWA Highway Safety Statistical Paper Synthesis report.(3)
Source: FHWA.(3)

## Slide 73: Systemic Approach: Screen and Prioritize Candidate Locations
Develop a prioritized list:
  Identify network elements.
  Conduct risk assessment.
  Prioritize locations.
Corridor | Route Type | Route Number | Start | End | Length (mi) | Average Daily Traffic
144.01 | CNTY | 89 | CSAH-30 | CSAH-30 | 1.4 | 480
40.04 | CSAH | 40 | New London Corp Limit | CSAH-2 | 5.9 | 450
131.01 | CNTY | 89 | CSAH-30 | MNTH-23 | 0.7 | 145
9.02 | CSAH | 9 | CR-90, Wilmar Corp Limit | CSAH-10 | 5.6 | 940
5.06 | CSAH | 5 | 150th Ave NW, CSAH-29 | CSAH-1 | 10.1 | 628
31.02 | CSAH | 31 | New London Corp Limit | MNTH-23 | 1.6 | 920
8.01 | CSAH | 8 | Renville County Line | Lake Lillian Corp Limit | 3.6 | 750
4.01 | CSAH | 4 | CSAH-8 | CSAH-20 | 6.7 | 320
2.05 | CSAH | 2 | CSAH-10 | MNTH-23 | 9.8 | 385
4.04 | CSAH | 4 | CR-98 | CSAH-40 | 2.4 | 290
38.01 | CSAH | 38 | CSAH-40 | CSAH-48 | 2.1 | 130
132.01 | CNTY | 89 | CSAH-8 | CSAH-8 | 2.2 | 190
42.01 | CSAH | 42 | CSAH-7 | County Line | 0.5 | 120
9.03 | CSAH | 9 | CSAH-10 | CSAH-40, Redwood St. | 4.9 | 1,800
25.01 | CSAH | 25 | CSAH-5 | USTH-71 | 3.2 | 1,315
CNTY = county; CSAH = county State-aid highway; MNTH = Minnesota trunk highway; CR = county road; USTH = U.S. trunk highway.
Source: FHWA. Modified by FHWA.(5)

## Slide 74: Systemic Approach: Screen and Prioritize Candidate Locations
Rank | Corridor | ADT Range | Road Departure Density | Access Density | Curve Critical Radius Density | Edge Risk | Totals
1 | 144.01 |  |  |  |  |  | 
2 | 40.04 |  |  |  |  |  | 
3 | 131.01 |  |  |  |  |  | 
4 | 9.02 |  |  |  |  |  | 
5 | 5.06 |  |  |  |  |  | 
6 | 31.02 |  |  |  |  |  | 
7 | 8.01 |  |  |  |  |  | 
8 | 4.01 |  |  |  |  |  | 
9 | 2.05 |  |  |  |  |  | 
= risk factor present.
ADT = average daily traffic.
Source: FHWA. Modified by FHWA.(5)

## Slide 75: Systemic Approach: Screen and Prioritize Candidate Locations
Chart: Number of Risk Factors Present
Length (%) | 0 | 5.8e-05 | 0.0010502 | 0.014853 | 0.072135 | 0.18051 | 0.27086 | 0.26552 | 0.14722 | 0.042995 | 0.0047959 | 0
RwD Crash Density | 0 | 0.0008962 | 0.0075811 | 0.015041 | 0.036582 | 0.064925 | 0.096247 | 0.13866 | 0.18979 | 0.24911 | 0.31219
Source: FHWA.

## Slide 76: Systemic Approach: Select Countermeasures
  Assemble comprehensive list of countermeasures.
  Evaluate/screen countermeasures.
  Select countermeasures for deployment.
Chevrons
Rumble Strips
High Friction Surface Treatments
Barriers
Clear Zones
All photos source: FHWA.

## Slide 77: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 1. Identify focus crash type.
Step 2. Identify contributing factors for focus crash type.
Step 3. Assemble list of potential countermeasures that address the crash type.
Step 4. Identify countermeasures that address the contributing factors associated with the focus crash type.
Step 5. Identify countermeasures with CMFs.
Step 6. Select countermeasure.

## Slide 78: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 1. Identify focus crash type:
  Select the focus crash type according to the priorities of the transportation agency (e.g., outlined in SHSP).
  Define focus crash type by:
    Type of maneuver (e.g., ROR).
    Time of day (day versus night).
    Type of segment (curve versus tangent) or type of intersection (e.g., four-leg signalized).

## Slide 79: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 2. Identify contributing factors for focus crash type. Some factors may be expected to increase a particular crash type: e.g., ROR crashes on curves during the daytime:
      Percent grade (as grade increases, crash potential increases).
      Average shoulder width (as shoulder width increases, crash
      potential decreases).

## Slide 80: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 3. Assemble list of potential countermeasures that address the crash type. Resources may include:
    National Cooperative Highway Research Program (NCHRP) Report 500 Series.(11)
    Highway Safety Manual.(12)
    FHWA CMF Clearinghouse.(13)
    FHWA Proven Safety Countermeasures list.(14)
    NHTSA Countermeasures That Work.(15)
    FWHA PedSafe.(16)
    FWHA BikeSafe.(17)
    State-generated list of common countermeasures within a State (i.e., “toolbox”).

## Slide 81: FHWA FCFT Report: Six-Step Countermeasure Selection
Source: FHWA.

## Slide 82: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 4. Identify countermeasures that address the contributing factors associated with the focus crash type:
  Compare the information known about each countermeasure on the
  list from step 3 to the contributing factors identified in step 2.
  Identify those countermeasures that specifically address one or
  more of the contributing factors.

## Slide 83: FHWA FCFT Report: Six-Step Countermeasure Selection
Countermeasure | Factor 1: Percent Grade | Factor 2: Average Shoulder Width
Install shoulder and/or centerline rumble strips |  | 
Widen lanes |  | 
Enhance curve delineation (chevrons, large arrows, or delineators on guardrails) |  | 
Install or improve curve warning signs (i.e., add flashing beacon) |  | 
Install warning arrows on pavement prior to curve |  | 
Install pavement markings to decrease speed prior to curve |  | 
Flatten horizontal curve (increase radius) |  | 
Flatten vertical curve (decrease grade) |  | 
Enhance pavement markings (edge lines) |  | 
Install skid-resistant pavement or improve pavement friction |  | 
Widen and/or pave shoulder |  | 
Install safety edge |  | 
Design safer slopes and ditches to prevent rollovers |  | 
Remove/relocate objects in hazardous locations |  | 
Delineate roadside objects |  | 
Improve design of roadside hardware (e.g., bridge rails) |  | 
Improve design and application of barrier and attenuation systems |  | 
 = countermeasure directly addresses risk factor.
Source: FHWA.(1)

## Slide 84: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 5. Identify countermeasures with CMFs. Resources may include:
    CMF Clearinghouse.(13)
    State CMF list.

## Slide 85: FHWA FCFT Report: Six-Step Countermeasure Selection
Countermeasure | Factor 1: Percent Grade | Factor 2: Average Shoulder Width | CMF Available
Install shoulder and/or centerline rumble strips |  |  | 
Widen lanes |  |  | 
Enhance curve delineation (chevrons, large arrows, or delineators on guardrails) |  |  | 
Install or improve curve warning signs (i.e., add flashing beacon) |  |  | 
Install warning arrows on pavement prior to curve |  |  | 
Install pavement markings to decrease speed prior to curve |  |  | 
Flatten horizontal curve (increase radius) |  |  | 
Flatten vertical curve (decrease grade) |  |  | 
Enhance pavement markings (edge lines) |  |  | 
Install skid-resistant pavement or improve pavement friction |  |  | 
Widen and/or pave shoulder |  |  | 
Install safety edge |  |  | 
Design safer slopes and ditches to prevent rollovers |  |  | 
Remove/relocate objects in hazardous locations |  |  | 
Delineate roadside objects |  |  | 
Improve design of roadside hardware (e.g., bridge rails) |  |  | 
Improve design and application of barrier and attenuation systems |  |  | 
 = countermeasure directly addresses risk factor; CMF for countermeasure available.
Source: FHWA.(1)

## Slide 86: FHWA FCFT Report: Six-Step Countermeasure Selection
Step 6. Select countermeasure. Select from the pool of eligible countermeasures generated in step 3.

## Slide 87: FHWA FCFT Quick Reference Guide: Countermeasures for Non-Intersection
Countermeasure | Contributing Factor |  |  |  |  |  |  | 
 | Larger Percent Grade | Narrower Lane Width | Narrower Paved Surface Width | Narrower Shoulder Width | Unpaved Shoulder | Higher Speed Limit | Mountainous Terrain | Smaller Curve Radius
Safety edge |  |  |  |  |  |  |  | 
Rumble strips/stripes |  |  |  |  |  |  |  | 
Enhanced friction for horizontal curves |  |  |  |  |  |  |  | 
Enhanced delineation for horizontal curves |  |  |  |  |  |  |  | 
Roadside design improvements at curves |  |  |  |  |  |  |  | 
Advance markings for curves |  |  |  |  |  |  |  | 
Advance signs |  |  |  |  |  |  |  | 
 = countermeasure directly addresses risk factor.
Source: FHWA.(2)

## Slide 88: FHWA FCFT Quick Reference Guide: Countermeasures for Intersection
Countermeasure | Contributing Factor | Contributing Factor |  |  |  | 
 | Smaller Curve Radius (for Intersection on Curve) | Wider Mainline Lane Width | Wider Mainline Median Width | Absence of Mainline Left Turn Channelization | Absence of Minor Street Right Turn Channelization (Signalized Intersections) | Higher Speed Limit/Design Speed
Left- and right-turn lanes |  |  |  |  |  | 
Yellow change intervals |  |  |  |  |  | 
Backplates with retroreflective borders |  |  |  |  |  | 
Application of multiple low-cost countermeasures |  |  |  |  |  | 
Advance signs |  |  |  |  |  | 
 = countermeasure directly addresses risk factor.
Source: FHWA.(2)

## Slide 89: Countermeasure Selection: Additional Resources
Systemic Project Selection Tool.(5)
Proven Safety Countermeasures list.(14)
CMF Clearinghouse.(13)
Pedestrian Safety Guide and Countermeasure Selection System.(16)
NCHRP 500 Series.(11)
Reliability of Safety Management Methods: Countermeasure selection.(18)
Highway Safety Manual (Part D).(12)
NHTSA’s Countermeasures That Work.(15)

## Slide 90: FHWA FCFT Report: Summary
Main goal—Inform applications of systemic safety improvements by identifying:
  Focus crash types.
  Focus facility types.
  Associated contributing factors.
Scope—There are three main technical tasks:
  Identify FCFTs—17 FCFTs (9 non-intersection and 8 intersection FCFTs).
  Identify contributing factors associated with the FCFTs.
  Develop a process to select countermeasures.
Source: FHWA.

## Slide 91: FHWA FCFT Report: Conclusions, Recommendations
Identifying FCFTs and risk factors:
  Agency with sufficient data and analysis capability:
    Develop agency-specific list of FCFTs.
    Identify risk factors.
  Agency with limited data and analysis capability:
    Refer to SHSP for focus crash types.
    Refer to the FCFT list and risk factors developed from the research.
Source: FHWA.

## Slide 92: FHWA FCFT Report: Conclusions, Recommendations
Using random forest to identify contributing factors, there is a limited ability to interpret the direction and form a relationship:
    This research: Simple approach looking for linear trend.
    Recommendation for future work: Exploring more effective ways to uncover the relationship.
Identifying contributing factors using the Bayesian approach shows significant potential—Causal Bayesian networks.
Source: FHWA.

## Slide 93: FHWA FCFT Report: Conclusions, Recommendations
Considering socioeconomic and weather factors:
  Potential for supporting informed decisions.
  Not enough theory to support or refute the results.
  More work in this area possibly needed.
Source: FHWA.

## Slide 94: Discussion
Source: FHWA.

## Slide 95: Polling Question
Q8
What is one takeaway from today’s presentation that you can use in your agency?
Source: FHWA.
Notes: Insert before summary slide
What is one takeaway, from today’s presentation, that you can use in your agency?
-Open response

## Slide 96: References
1 Saleem T., R. Porter, R. Srinivasan, D. Carter, S. Himes, and T. Le. 2020. Contributing Factors for Focus Crash and Facility Types. Report No. FHWA-HRT-20-052. Washington, DC: Federal Highway Administration. https://www.fhwa.dot.gov/publications/research/safety/20052/index.cfm, last accessed October 21, 2021.
2 Porter, R., T. Le, F. Gross, D. Carter, Saleem T., and R. Srinivasan. 2020. Contributing Factors for Focus Crash and Facility Types: Quick Reference Guide. Report No. FHWA-HRT-20-053. Washington, DC: Federal Highway Administration. https://www.fhwa.dot.gov/publications/research/safety/20053/20053.pdf, last accessed October 28, 2021.
3 Donnell E., E. Hanks, R. J. Porter, L. Cook, R. Srinivasan, F. Li, M. Nguyen, and K. Eccles. The Development of Crash Modification Factors: Highway Safety Statistical Paper Synthesis. Report No. FHWA-HRT-20-069. Washington, DC: Federal Highway Administration. https://www.fhwa.dot.gov/publications/research/safety/20069/index.cfm, last accessed October 21, 2021.
4 FHWA. 2016. Electronic Code of Federal Regulations. 23 CFR §924.3 Definitions.
5 Preston, H., R. Storm, J. D. Bennett, and B. Wemple. 2013. Systemic Safety Project Selection Tool. Report No. FHWA-SA-13-019. Washington, DC: Federal Highway Administration. https://safety.fhwa.dot.gov/systemic/fhwasa13019/, last accessed October 21, 2021.
6 NHTSA. 2018. “Fatality Analysis Reporting System (FARS)” (website). https://www.nhtsa.gov/research-data/fatality-analysis-reporting-system-fars, last accessed January 19, 2018.
7 FHWA. n.d. “HSIS” (website). https://www.hsisinfo.org/, last accessed October 21, 2121.
8 R Core Team. 2014. R: A language and environment for statistical computing (software). Vienna, Austria: R Foundation for Statistical Computing. http://www.R-project.org/, last accessed October 28, 2021
9 Barrowman, N., S. Gatscha, and F. Momoli. 2021. vtree: Display Information About Nested Subsets of a Data Frame (software). https://CRAN.R-project.org/package=vtree, last accessed October 28, 2021.

## Slide 97: References
10 Breiman, L., A. Cutler, A. Liaw, and M. Wiener. 2018. randomForest: Breiman and Cutler's Random Forests for Classification and Regression (software). https://CRAN.R-project.org/package=randomForest , last accessed October 28, 2021.
11 NCHRP. 2003–2009. “NCHRP Report 500: Guidance for Implementation of the AASHTO Strategic Highway Safety Plan” (website). https://www.trb.org/Main/Blurbs/152868.aspx, last accessed October 28, 2021.
12 AASHTO. 2010. Highway Safety Manual. Washington, DC: American Association of State Highway and Transportation Officials. http://www.highwaysafetymanual.org/Pages/default.aspx, last accessed October 21, 2021.
13 FHWA. 2018. “CMF Clearinghouse. 2018” (website). http://www.cmfclearinghouse.org, last accessed October 21, 2021.
14 FHWA. 2017. “Proven Safety Countermeasures” (website). https://safety.fhwa.dot.gov/provencountermeasures, last accessed October 21, 2021.
15 Goodwin, A., B. Kirley, L. Sandt, W. Hall, L. Thomas, N. O’Brien, and D. Summerlin. 2013. Countermeasures That Work: A Highway Safety Countermeasure Guide for State Highway Safety Offices, Seventh Edition. Report No. DOT-HS-811-727. Washington, DC: National Highway Traffic Safety Administration. http://www.nhtsa.gov/staticfiles/nti/pdf/811727.pdf, last accessed October 21, 2021.
16 FHWA. 2018. “PEDSAFE: Pedestrian Safety Guide and Countermeasure Selection System” (website). http://www.pedbikesafe.org/PEDSAFE, last accessed October 21, 2021.
17 FHWA. 2018. “BIKESAFE: Bicycle Safety Guide and Countermeasure Selection System” (website). http://www.pedbikesafe.org/bikesafe, last accessed October 21, 2021.
18 Gross, F., T. Harmon, G. Bahar, and K. Peach. 2016. Reliability of Safety Management Methods: Systemic Safety Programs. Report No. FHWA-SA-16-041. Washington, DC: Federal Highway Administration. https://safety.fhwa.dot.gov/rsdp/downloads/fhwasa16041.pdf, last accessed October 28, 2021.

## Slide 98: Contacts
Roya Amjadi
Roya.Amjadi@dot.gov
Office of Safety Research Development, Federal Highway Administration